## Slide 1
NUS EE5003 · 2026-10-13
Intelligent Multi-Agent
Literature Research Assistant
Phase 0 Progress Report · Context & Harness Engineering
智能多智能体文献研究助手 · Phase 0 进展汇报
Group meeting · supervisor + research group · 21 slides
① Selection
② Hard problems
③ Evidence
Every number reproducible · evidence in prototype/out/ · decision gate is a separate handout
Notes: Twenty-one slides, three parts: how the stack was chosen, the six problems the design has to survive, and eight feasibility checks that were actually run in Phase 0. Everything shown is measured, and every number traces to a file in the prototype tree.

## Slide 2
CONCLUSION FIRST
Viable, verified, ready for Phase 1
结论先行：选型可行、闭环跑通
Phase 0 meets its targets: fast stores, precise guards, cheap runs
Storage — graph 2-hop p95 4.42 ms; three stores hold 5k papers in 64.9 MB
Guards — 15 of 15 injected faults detected, 0 false alarms on normal runs
Loop — $0.006 per run with every claim citable; resume point is the node boundary
Sources
whitelist-first retrieval
over target venues
whitelist recall 386 papers / 3 y
arXiv-in-OpenAlex 91.7%
Closed loop
a report that can be audited
100% of claims citable
8.9k–10.8k characters
16–23 claims per run
Self-correction
guards proven by injection
5 fault families × 3 runs
detection 1.00
false positives 0
Three stores hold at 5k papers (64.9 MB) · resume granularity = node boundary · checkpoint 4 KB per step
Phase 0 targets met — ready to start Phase 1
Phase 0 Progress Report · EE5003 · NUS
02 / 21
Notes: Phase 0 targets are met. The stores hold at five thousand papers, the guards fire on every injected fault with no false alarms, and one topic runs end to end for about six tenths of a cent. The three-store split stands, no store swap is needed, and the only miss — vector latency — is attributable to the embedded deployment mode rather than to the architecture. On that basis Phase 1 can start.

## Slide 3
MODULE MAP
Ten modules, ten decisions
模块选型总表：十行定稿
#
Module
Choice
1
Orchestration
LangGraph
2
Gateway
LiteLLM (in-process SDK)
3
Local inference
Ollama / vLLM (deferred)
4
Graph store
Kuzu (embedded)
5
Vector store
Qdrant (local)
6
Sources & parsing
OpenAlex + arXiv, own parsing
7
Scheduling
APScheduler
8
Web backend
FastAPI
9
Frontend
Vue3 + Vite + ECharts
10
Evaluation
DeepEval + custom event metrics
Framework-first rows — 1 Orchestration: LangGraph · 2 Gateway: LiteLLM (in-process SDK)
Rows 3–10 — local inference (deferred) · Kuzu · Qdrant (local) · OpenAlex + arXiv · APScheduler
FastAPI · Vue3 + Vite + ECharts · DeepEval + custom event metrics
Framework-first where it matters
03 / 21
Notes: Ten rows, ten decisions. Two are framework-first: LangGraph for orchestration and LiteLLM as an in-process gateway. The other eight are deliberately boring — local inference is deferred, Kuzu for the graph, Qdrant local for vectors, direct OpenAlex and arXiv clients with our own parsing, APScheduler, FastAPI, Vue 3, and DeepEval plus a custom event metric layer. Every row has a measurement behind it, which is what slides 14 to 21 show.

## Slide 4
LANGCHAIN VS THIS PROJECT
Mostly a wrapper layer, not an engine
LangChain 各模块 vs 本项目选型
Module
LangChain part
What it is
Ours
Orchestration
LangGraph (its own engine)
engine
LangGraph adopted
Gateway
provider model classes
vendor-SDK wrapper
LiteLLM
Sources & parsing
community loaders
pypdf / Unstructured wrapper
direct clients, own chunker
Retrieval
retrievers
hidden pipeline
filter, dedup, novelty
Stores
vectorstore wrappers
trimmed capability
official clients
Memory & agents
langchain-classic
legacy, superseded
LangGraph checkpoints
Evaluation & tracing
LangSmith
SaaS
DeepEval + event table
Service & tracing
langserve / callbacks
route wrapper
own FastAPI + events
Why ours fits — full-strength capability (payload filters, local mode, quantisation) · prompts and tool formats stay visible
no version matrix to maintain · every wrapper replaced by the client it wrapped
v1 moved chains, AgentExecutor and memory into langchain-classic; LangGraph became the orchestration core
Same libraries, one less layer
04 / 21
Notes: Most of LangChain is a wrapper layer, not an engine: community loaders wrap pypdf, retrievers hide the pipeline, vectorstore wrappers trim capability. We keep the two parts that are real engines — LangGraph and the provider model classes — and write the rest ourselves so nothing important is hidden. The v1 migration made this explicit by moving chains, AgentExecutor and memory into langchain-classic and making LangGraph the orchestration core.

## Slide 5
ORCHESTRATION
A state machine, not a chat room
编排内核三选一
Dimension
LangGraph
AutoGen
OpenAI Agents SDK
Control flow
explicit nodes + conditional edges
decided by dialogue turns
driven by handoffs
Recovery point
checkpointer at node boundary
session level
sessions only
Observability
LangSmith (optional)
events + tracing
reports to OpenAI
Vendor neutrality
change base_url
multi-vendor
OpenAI-first
Built for — product backends embedding LLM flows (chosen) · multi-agent conversation research (AutoGen)
shipping agent apps fast (OpenAI Agents SDK, kept for the Chat page)
Why not the others — AutoGen hides control flow in dialogue turns and was rewritten in v0.4;
OpenAI Agents SDK is OpenAI-first and its guardrails are input/output checks, not stage guards
LangGraph chosen
05 / 21
Notes: The choice is between a state machine, a chat room, and a vendor SDK. AutoGen hides control flow inside dialogue turns and was rewritten in v0.4; the OpenAI Agents SDK is OpenAI-first and its guardrails are input/output checks rather than stage guards. LangGraph wins because control flow is explicit, recovery happens at node granularity, state is inspectable, and the runtime stays vendor-neutral.

## Slide 6
GATEWAY
A transport layer we can audit
网关三选一
Dimension
LiteLLM (chosen)
Self-built thin
OpenRouter
Interface
in-process, no new service
own ~300 lines
third-party hop
Retries and cost
cost table + health cooldown
self-maintained
hidden failover
Fit here
one protocol implementation
framework-first conflict
data hop, no local engines
Our thin layer on top — content-addressed cache · truncation detection · budget breaker
every call written as an event (tokens, cost, latency, cache hit)
Why not self-built (~300 lines) — 100+ provider adapters, price tables and retry policy
would all become our maintenance burden
OpenRouter in one line — hosted aggregator: one key, many models, auto-failover, data-policy filters;
not here because of the data hop, no local engines and hidden failures; kept for model benchmarking
LiteLLM chosen, in-process
Phase 0 Progress Report · EE5003 · NUS
06 / 21
Notes: LiteLLM runs in-process, so there is no extra service to operate, and it brings price tables, retries and health cooldowns for a hundred-plus providers. On top we keep a thin layer of our own: a content-addressed cache, truncation detection, a budget breaker, and one event per call carrying tokens, cost, latency and cache hit. OpenRouter is kept only for one-off model benchmarking — its data hop, lack of local engines and hidden failures are not acceptable in the main path.

## Slide 7
WEEKLY-RUN GRAPH
Ten nodes, guards between them
周更状态图：节点与守卫
S0 scope_check
validate scope
S1 plan
subtasks
S2 retrieve
evidence cards
S3 ingest_parse
parse + chunk
S4 map_update
idempotent writes
G1 drift
G2 scope
G4/G5 loop
G7 citation
G8 budget
S5 novelty
diff vs last week
S6 analyze
cited findings
S7 draft
report + claims
S8 critique
cross-vendor review
S9 finalize
persist report
Back-edges
scope fail → S1
stagnation → S1 replan
critique below threshold → S7 rewrite
budget exceeded → S9 finalize-or-abort
checkpoint per node — resume = node boundary
ladder
retry → degrade → replan → abort
The full E1–E13 edge table lives in the design doc; this page shows only the four most instructive edges
Guards sit between the nodes
Phase 0 Progress Report · EE5003 · NUS
07 / 21
Notes: Ten nodes and five guard diamonds. S0 validates scope, S1 plans, S2 retrieves, S3 parses and chunks, S4 writes to the stores idempotently, S5 diffs against last week, S6 analyses with citations, S7 drafts the report and claims, S8 critiques with a second vendor, S9 finalises and persists metrics. Four edges come back: a scope failure or stagnation returns to S1, a critique below threshold returns to S7, and an exhausted budget finalises or aborts with an annotation. The spine across every node is the same: a checkpoint per node, so resume equals node boundary, and the escalation ladder retry, degrade, replan, abort.

## Slide 8
PROBLEM 1 · ANTI-DRIFT
How we keep a weekly run on topic
如何防止 agent 走偏
A versioned Scope Anchor with a calibrated boundary
scope is a stored object the harness can check — not an instruction the model is asked to respect
Problem
early drift is amplified downstream, and “zero drift” cannot be promised; detection must be bounded,
detectable, reversible and measurable
Methods — seven levers, all deterministic
Scope Anchor（范围锚点） — one object: statement, boundaries, counter-examples, version-stamped into every node
Seed-corpus centroid（种子语料质心） — the anchor becomes a mean embedding, so drift is a cosine distance
Stage contracts（阶段契约） — input/output schema per stage with validators; a stage cannot be skipped
Role split + cross-vendor critic（角色分离） — each agent sees only what it needs; the critic never writes
Evidence-first（证据优先） — every claim carries a citation resolvable in the corpus snapshot
Hard limits in code（代码内硬约束） — whitelist, time window, dedup fingerprints; never in prompts
Cross-week anchoring（跨周锚定） — persist track state, diff against last week, flag slow drift
Retrieval and the drift guard share one anchor object, so scope never forks; a new topic costs one recalibration.
→ evidence: slide 20 — the two calibrated thresholds, and the counter-example that forced the representation change
Detected, reversible, measured
Phase 0 Progress Report · EE5003 · NUS
08 / 21
Notes: Early drift is amplified downstream, so the mechanism has to be explicit. The Scope Anchor is one versioned object holding the statement, the in-scope boundaries and the counter-examples; it is injected into every node's system slot. Crucially, the retrieval scorer and the drift guard read the same object, so scope can never fork into two definitions — which also means a new topic costs one recalibration instead of a rewrite, and old runs stay readable against the anchor version they ran on.
The representation matters as much as the anchor: the scope is stored as a mean embedding of the accepted seed papers, so "is this still on topic" becomes a cosine distance rather than a judgement call by the model. Around that sit stage contracts with per-stage validators, a role split where the cross-vendor critic never writes, evidence-first claims, hard limits such as the source whitelist and dedup fingerprints enforced in code rather than in prompts, and cross-week anchoring where per-topic state is persisted and diffed against last week so slow drift shows up as a trend. The thresholds themselves are calibrated on real corpora — slide 20 shows the arithmetic.

## Slide 9
PROBLEM 2 · LOOPS AND STAGNATION
How it notices it is going in circles
死循环与停滞：检出与处置
Cheap repetition signatures plus a bounded ladder
a loop is replanned once, then stopped by the state machine — not by a wall-clock timeout
Problem
the same query re-issued, zero new facts, cost rising with no output, and nobody watching an
unattended run
Methods — five detectors, two exit rules
Signature window（签名窗口） — tool name + normalised argument hash, window k=5, firing at repeat ≥ 3
State-hash repetition（状态哈希重复） — the same state reached twice means the graph has paid twice
Facts delta = 0（事实增量归零） — a verified-fact set that stops growing marks stagnation directly
Bounded back-edges（有界回边） — a limited number of replans per node, counted in state, never unbounded
Escalation ladder（升级阶梯） — first hit replans with a recovery packet; a second hit aborts
Both detectors read only the event log and the state hash, so policing a loop adds no tokens to the run being policed.
→ evidence: slide 20 — injected repeated-call and zero-progress scenarios, plus the normal-run false-alarm count
First replan, then hard stop
Phase 0 Progress Report · EE5003 · NUS
09 / 21
Notes: An unattended run that re-issues the same query, adds no facts and keeps spending is the failure mode here. Five detectors cover it without any model call: a signature window over tool name plus a normalised argument hash, with window five and a repeat threshold of three; state-hash repetition, which catches the graph returning to a place it has already paid for; a facts delta of zero, which catches stagnation before it even looks like a loop; bounded back-edges, so re-entry cannot be unbounded; and an escalation ladder that replans once with a recovery packet and aborts with an annotation on the second hit. Because both primary detectors read only the event log and the state hash, policing a loop adds no tokens to the run being policed.

## Slide 10
PROBLEM 3 · BUDGET
How it stops burning money
预算失控：四维看门狗
A four-meter watchdog that degrades before it stops
tokens · seconds · cost · steps, re-read after every call — the ceiling is enforced by the harness
Problem
an unattended run has no natural cost ceiling, and “let it finish” is the wrong default when the meter is
the only thing still moving
Methods — a watchdog with teeth
Four meters（四维计量） — tokens · seconds · cost · steps, re-read after every model and tool call
Budget from config（配置注入） — declared per topic and overridable, so a costly topic cannot inherit a cheap default
Early degradation（提前降级） — cheaper model tier and shorter retrieval batches before the ceiling, not after
Two rungs（两级阈值） — warn at 80% is non-blocking; stop at 100% halts the graph and annotates the report
Event per decision（逐决策留痕） — each reading emits a metric event, each verdict a guard_trigger
The watchdog chooses the rung, the state machine executes it: retry → degrade → replan → abort is data, not code paths.
→ evidence: slide 18 (checkpoint cost per super-step) and slide 20 (the budget scenario)
Warn at 80%, stop at 100%
Phase 0 Progress Report · EE5003 · NUS
10 / 21
Notes: There is no natural cost ceiling in an unattended run, and "let it finish" is the wrong default when the meter is the only thing still moving. The watchdog reads four meters — tokens, seconds, cost and steps — after every model and tool call, with ceilings declared per topic and overridable there so an expensive topic cannot inherit a cheap default. Before the ceiling it degrades: a cheaper model tier and shorter retrieval batches. At eighty percent it warns without blocking; at a hundred percent it stops and annotates the report, because a partial report beats a burnt budget. Every reading emits a metric event and every verdict a guard trigger, so the ladder is auditable afterwards. Related ceilings — per-node timeout and the graph recursion limit — live in the same config block, and the ladder itself is data: the watchdog chooses the rung, the state machine executes it.

## Slide 11
PROBLEM 4 · HALLUCINATION
No unsupported claim ships
如何控制幻觉与事实性
Factuality is enforced by contract and by resolvable citations
a claim that cannot be traced into the corpus snapshot never leaves the node
Problem
long chains invite fabricated numbers and silent contradictions, and “be careful” is not a mechanism
anyone can test
Methods — factuality enforced at six points
Claim + evidence are one unit（声明与证据同体） — the schema rejects a claim with no citation field
Citations must resolve（引用可回查） — paper_id + snippet must be found in the corpus snapshot
Contradictions are first-class（矛盾显式保留） — the report presents the disagreement, never a silent average
Refusal is legal（允许拒答） — “insufficient evidence” is accepted, but must name what is missing
Numbers carry provenance（数字带出处） — every number comes from a tool result; no silent source wins
Cross-vendor critique（跨模型评审） — a second vendor re-reads each claim against its cited snippet
The resolver reads the same snapshot the retrieval used, so a citation that resolves today survives a re-import.
→ evidence: slides 20–21 — citation-resolvable rate, grounding, and the metric caveat
Unsupported claims cannot pass
Phase 0 Progress Report · EE5003 · NUS
11 / 21
Notes: Factuality is enforced by contract, not by tone. Claim and evidence are one unit, so the schema rejects a claim object with no citation field and an unsupported sentence cannot reach the report stage at all. Citations must resolve: the paper id plus snippet has to be found in the corpus snapshot, or the claim is marked unverified and counted into the hallucination rate. Contradictions are first-class — when sources disagree the report presents the disagreement instead of a silent average. Refusal is legal, provided it names what is missing and what would settle the question. Numbers carry provenance from tool results, with no source silently winning over another, and a second vendor's model re-reads each claim against its cited snippet before finalize, without the ability to rewrite it. The resolver reads the same snapshot the retrieval used, so a citation that resolves today survives a re-import.

## Slide 12
PROBLEM 5 · CONTEXT GROWTH
Keep a long run inside the window
长跑上下文膨胀：折叠与分层
State holds summaries and pointers; folding is an explicit node
raw text never enters the window, so context size is a design decision instead of a side effect
Problem
a run spans hours, so state, tool results and retrieval history grow without bound — and on-device
tiers are tighter still
Methods — fold explicitly, store pointers
Summaries and pointers only（只存摘要与指针） — state keeps paper_id and event ids, never raw text
Budget before every call（调用前算预算） — the budget of a call is computed from the state that call receives
Folding rules（折叠规则） — history becomes points + citations; old dialogue becomes a summary
Three-layer memory（三层记忆） — topic state / evidence stores / report history, each with its own interface
Fixed injection slots（固定注入槽） — system (scope + state + policy) / user (task) / tools (cards)
Folding is auditable（折叠可审计） — every fold emits before/after token counts into the event log
Status: designed and instrumented, not yet measured — Phase 0 data volume is too small to stress the window.
→ evidence: slide 18 — the checkpoint that makes restart cost independent of run length
Fold first, then route
Phase 0 Progress Report · EE5003 · NUS
12 / 21
Notes: A run spans hours, so state, tool results and retrieval history grow without bound — and on-device tiers are tighter still. State keeps summaries and pointers only: paper ids and event ids, with raw text left in the filesystem and the stores and re-read on demand. The token budget of a call is computed from the state that call will receive, and folding is an explicit node rather than an implicit behaviour. The folding rules are fixed: retrieval history becomes structured points plus citations, old dialogue becomes a sliding window plus a summary, and long documents never enter whole. Memory is layered into topic state, evidence stores and report history, each with its own read interface, and prompt assembly uses fixed slots — system, user, tools — so it stays deterministic. Every fold emits before and after token counts, which turns window pressure into a number. Status: designed and instrumented, not yet measured, because Phase 0 data volume is too small to stress the window.

## Slide 13
PROBLEM 6 · TOOL AND MCP RETURNS
How we validate what tools return
如何验证工具/MCP 返回的数据是否合法
Six validation layers, and the first four need no LLM
whatever schema or arithmetic can decide is decided without a model call; critical actions fail closed
Problem
tool output is untrusted data, and one word, “reasonable”, hides four questions: protocol validity,
numeric domains, cross-field consistency, semantics
Methods — a six-layer pipeline, cheapest layer first
L0 protocol（协议层） — JSON-RPC validity, isError, output schema, types and enums via Pydantic
L1 domain rules（域规则层） — 0 ≤ ratio ≤ 1 · cited_by ≥ 0 · year ≤ current · published ≤ updated
L1 continued（域规则·续） — citation resolvable in the store · unit normalisation · whitelist · freshness · dedup
L2 cross-source recompute（跨源重算） — key numbers recomputed from an independent second source
L3 statistical anomaly（统计异常） — z-score and IQR against history, plus count spikes
L4 LLM for semantics only（仅语义用 LLM） — rubric-based, cross-vendor, sampled and cached
L5 human spot-check（人工抽检） — calibrates the judge, not the data
A failed layer means no graph write, no evidence-pool entry, no report claim; the same validators wrap our own nodes.
→ evidence: slide 21 — the injection runs used to check interception and false positives
No LLM until layer four
Phase 0 Progress Report · EE5003 · NUS
13 / 21
Notes: Tool output is untrusted data, and one word, "reasonable", hides four different questions: protocol validity, numeric domains, cross-field consistency, and semantics. The pipeline answers them cheapest-first. L0 checks JSON-RPC validity, the error flag, output schema, types and enums with Pydantic before a single field is read. L1 applies domain rules: ratios between zero and one, non-negative citation counts, year not in the future, published not after updated, citations resolvable in the local store, unit normalisation, source whitelist, freshness and dedup. L2 recomputes key numbers from an independent second source — OpenAlex against Crossref against the local graph. L3 flags statistical anomalies by z-score and IQR against history, plus count spikes. Only then does L4 use an LLM, and only for semantics: rubric-based, cross-vendor, sampled and cached. L5 is a human spot check that calibrates the judge rather than the data. A failed layer means no graph write, no evidence-pool entry and no report claim, and the same validators wrap our own node outputs.

## Slide 14
VERIFICATION 1 · SOURCES (S1)
Can the whitelist see the venues?
验证 1：数据源覆盖度
The whitelist does reach our target venues, and arXiv is indexed there
386 papers / 3 years (≈129/yr, a floor) · arXiv-in-OpenAlex 91.7% · relevance 10/10 · 20/20 HTTP 200, p50 1.09 s
How we measured
测量方法
counted whitelist-venue recall over three years; matched arXiv
preprints to OpenAlex by DOI; hand-scored relevance; probed
the polite-pool limit with 20 requests
Results
实测结果
whitelist 386 papers / 3 years (≈129/yr, a floor); arXiv 91.7%;
relevance 10/10; 20/20 HTTP 200, p50 1.09 s
Caveat — NeurIPS / ICLR / OSDI records are missing
Formulas
计算公式
papers_per_year = 386 / 3 ≈ 129
年召回下界
coverage = matched / sampled = 0.917
arXiv 命中率
p50 = percentile(latency, 50)
延迟中位数
Impact
结论影响
whitelist filtering must be primary; arXiv is a freshness supplement, not a gap-filler
Sources verified
Phase 0 Progress Report · EE5003 · NUS
14 / 21
Notes: The measurement is simple: count whitelist-venue recall over three years from the twelve configured source ids, match arXiv preprints to OpenAlex records by DOI, hand-score sampled relevance, and probe the polite-pool rate limit with twenty sequential requests while recording status and latency percentiles. The whitelist returns 386 papers over three years, about 129 a year, and that is a floor because NeurIPS, ICLR and OSDI records are missing from the count; ninety-one point seven percent of arXiv preprints are indexed in OpenAlex; the relevance spot-check was ten out of ten; and all twenty requests returned HTTP 200 with a median of 1.09 seconds. The conclusion is that whitelist filtering must be the primary retrieval channel, with arXiv as a freshness supplement rather than a gap-filler.

## Slide 15
VERIFICATION 2 · RETRIEVAL AND DEDUP (S1b)
Which strategy, how much reference data?
验证 2：检索 / 去重 / 引用完整率
Retrieval needs both strategies, and a stronger dedup key
overlap 0.004–0.014 · duplicates 19.3–19.8% · reference completeness 1.5% / 14.3% vs broad 25–27%
How we measured
测量方法
ran broad, whitelist and expansion strategies over the same
window (994 records); compared result sets by title; counted
duplicate groups; probed incremental cursors
Results
实测结果
expansion adds 126/155 papers; references sit in 25–27% of
broad records vs 1.5% / 14.3% whitelist; updated_date is paid
(429), publication_date + cursor is stable
Caveat — a 2050 date appeared; date filtering is mandatory
Formulas
计算公式
J(A,B) = |A ∩ B| / |A ∪ B|
= 0.014 (T1) / 0.004 (T2)
结果集重合度
dup_rate = 101/511, 93/483
同标题重复率
ref_completeness = 1.5% / 14.3%
引用完整率
new = |E \ W| = 126 / 155
扩展查询新增数
Impact
结论影响
whitelist + multi-query expansion; DOI+title+year dedup with merged_ids; reverse cited_by edges
Retrieval plan fixed
Phase 0 Progress Report · EE5003 · NUS
15 / 21
Notes: Comparing broad, whitelist and expansion strategies over the same window produced 994 records. Overlap between whitelist and broad recall is a Jaccard of 0.014 on one topic and 0.004 on the other — essentially disjoint corpora, which is why both strategies are needed and why whitelist filtering is not merely denoising. Same-title duplicates run at 19.8 and 19.3 percent, so a sha1 of the canonical id is not enough: the dedup key is DOI plus normalised title plus year, with merged ids kept on the surviving record. Reference completeness is the counter-intuitive one: broad records carry references 25 to 27 percent of the time, whitelist records only 1.5 and 14.3 percent, and a DOI cross-check across all versions showed this is a property of the source record, not a version artefact. That is why reverse cited_by edges and a Crossref supplement are planned. Expansion adds 126 and 155 papers, and the incremental API picture is: the updated-date filter is a paid feature returning 429, while publication date with a cursor is stable with zero page overlap. A 2050 publication date also appeared, so date sanity filtering is mandatory at ingest.

## Slide 16
VERIFICATION 3 · STORAGE STACK (S3)
Do three stores survive 5k papers?
验证 3：存储栈（三库）
The three-store split holds at 5,000 papers
graph 2-hop p95 4.42 ms · author agg p95 5.06 ms · SQLite p50 0.07 ms · growth 0 · disk 64.9 MB
How we measured
测量方法
imported 5,000 records into SQLite, Kuzu and Qdrant; ran four
query classes 30 rounds each; re-imported the batch; rebuilt
the indexes from the truth source
Results
实测结果
all 20,000 edges via MATCH+MERGE; rebuild reproduced
identical counts; single-writer semantics confirmed; import
times sqlite 0.22 s / qdrant 26.78 s / kuzu 169.46 s
Caveat — a stale Kuzu DB inflated counts (631 vs 957)
Formulas
计算公式
p95 = percentile(latency, 95)
95 分位延迟
growth = after − before = 0
幂等零增长
disk = 12.89 + 49.06 + 2.95 = 64.90 MB
磁盘合计
Impact
结论影响
no store swap needed; count reconciliation became mandatory; vector latency moves to Phase 1
Storage decided
Phase 0 Progress Report · EE5003 · NUS
16 / 21
Notes: Five thousand real records were imported into SQLite, Kuzu and Qdrant, four query classes were run thirty rounds each, the batch was re-imported to test idempotency, and the indexes were deleted and rebuilt from the truth source. Graph two-hop p95 is 4.42 milliseconds, author aggregation p95 5.06 milliseconds, SQLite lookup p50 0.07 milliseconds; twenty thousand edges were written through match-and-merge; the rebuild reproduced identical counts; re-import grew every count by zero; total disk is 64.9 megabytes, split 12.89 for Kuzu, 49.06 for Qdrant and 2.95 for SQLite. Two silent traps surfaced: a stale Kuzu database inflated author counts to 957 against the true 631, and Kuzu only flushes on database close, which produced a false zero-megabyte reading. The verdict is that no store swap is needed, count reconciliation became mandatory, and the vector-latency item moves to Phase 1.

## Slide 17
VERIFICATION 4 · VECTOR LATENCY (S3b)
Why vector search missed its target
验证 4：向量检索延迟归因
155 ms is a deployment-mode property, not an architecture flaw
pure math floor 0.65 ms (0.3%) · Python glue ~26% · payload filtering +140 ms (74%) · local mode has no ANN
How we measured
测量方法
read the local-mode implementation (0 hits for HNSW, 0 for
np.dot); ran an attribution probe at 5,000 points / 1,024 dims;
added a scale curve from 1,250 to 5,000
Results
实测结果
local without filters 49.91 ms p50; payload indexes have no
effect in local mode; year>=2020 matches all 5,000 points yet
costs +112 ms, so cost tracks scanned points
Caveat — 100 ms assumed a production ANN engine
Formulas
计算公式
share = 0.65 / 189.32 ≈ 0.3%
纯算力占比
overhead_filter ≈ +140 ms (74%)
过滤开销
slope = Δt / Δpoints ≈ 0.038 ms/point
线性斜率
t(20k) ≈ 0.038 ms × 20000 ≈ 0.76 s
规模外推
Impact
结论影响
exact kNN (higher recall, slower); deployment mode + target recalibration move to Phase 1
Not a design flaw
Phase 0 Progress Report · EE5003 · NUS
17 / 21
Notes: Vector top-ten latency was 155 milliseconds against a 100 millisecond target, so the question was whether the architecture or the measurement was at fault. Reading the local-mode implementation settled it: HNSW appears zero times and numpy dot zero times — the embedded mode is a Python scan with no ANN index, and payload indexes have no effect there. The attribution probe at five thousand points and 1024 dimensions shows the pure-math floor is 0.65 milliseconds, about 0.3 percent of the total; the Python glue costs about 26 percent, since even the unfiltered path takes 49.91 milliseconds; and payload filtering adds around 140 milliseconds, 74 percent. Notably, a year filter that matches all five thousand points still costs 112 milliseconds, so filter cost tracks scanned points, not selectivity. The scale curve gives about 0.038 milliseconds per point, extrapolating to roughly 0.76 seconds per query at twenty thousand papers. So this is exact kNN — higher recall, slower — and the deployment decision plus target recalibration belong to Phase 1.

## Slide 18
VERIFICATION 5 · CRASH RESUME (S4)
Six scenarios, three hard kills
验证 5：断点续跑
Node-boundary resume reproduces the run; replaying input does not
invoke(None) matched the control state field by field · events 1..N across 3 kills · checkpoint 28–37 KB
How we measured
测量方法
ran six scenarios (control, single crash, double crash, input
drift, re-trigger, correct resume) with deterministic os._exit(9)
kills; compared final states
Results
实测结果
invoke(None) reproduces the control state field by field;
passing the full input replays from START (fetch ran 2–3
times); crashed nodes always re-run
Caveat — events stayed contiguous (1..N) across 3 kills
Formulas
计算公式
resume_ok = (state_resumed == control)
状态逐字段一致
ckpt_per_step = bytes / steps ≈ 4 KB
单步检查点
gaps = N_expected − N_observed = 0
事件序号无缺口
Impact
结论影响
node idempotency is a hard requirement; a resume guard (G15) covers drift and re-triggering
Resume rule book
Phase 0 Progress Report · EE5003 · NUS
18 / 21
Notes: Six scenarios ran with deterministic hard kills rather than simulated exceptions: control, single crash, double crash, input drift, re-trigger, and correct resume. Calling invoke with no input reproduces the control state field by field, and events stayed contiguous from one to N across three kills — which is what makes the event log usable as the post-crash truth source. Passing the full input, however, replays from the start: fetching ran two to three times. Crashed nodes always re-run, and neither input drift nor re-triggering of a finished run is blocked by the framework. Checkpoints are 28 to 37 kilobytes per run, about four kilobytes per super-step. Two requirements came out of this: node idempotency is now mandatory, and a resume guard was added for input drift and re-triggering.

## Slide 19
VERIFICATION 6 · CLOSED LOOP (S5)
From topic to citable report
验证 6：单 topic 端到端闭环
One topic becomes a verifiable report for about a cent
100% of claims citable · 8.9k–10.8k characters, 16–23 claims · $0.0036–0.0126 cold in 60–91 s · $0 cached
How we measured
测量方法
one HTTP request fetched 24 real OpenAlex records with
abstracts; the full chain ran locally; cost and latency come from
the event log; the run was repeated on a warm cache
Results
实测结果
report 8.9k–10.8k characters, 16–23 claims, all citable; cold
start $0.0036–0.0126 in 60–91 s; cached rerun $0 in 0.1 s with
byte-identical claims; 33–34 events per run
Caveat — small max_tokens returns an empty body
Formulas
计算公式
cost_run = Σ(in × p_in + out × p_out)
单次成本累加
citable_rate = citable / claims = 1.0
可回查引用率
saving = 1 − cost_cached / cost_cold = 1
缓存节省
Impact
结论影响
feasible and cheap; the gateway must catch truncation that looks like an empty success
Loop feasible and cheap
Phase 0 Progress Report · EE5003 · NUS
19 / 21
Notes: One HTTP request fetched twenty-four real OpenAlex records with abstracts, and the full chain then ran locally: normalise, dedup, chunk, store, retrieve, LLM card extraction, LLM report, citation check, events. Cost and latency come from the event log, and the run was repeated against a warm cache to separate API cost from model cost. The report is 8.9 to 10.8 thousand characters with 16 to 23 claims, all of them citable; a cold start costs between $0.0036 and $0.0126 in 60 to 91 seconds; a cached rerun costs nothing in about a tenth of a second with byte-identical claims; each run writes 33 to 34 events. The loop is feasible and cheap. One gateway behaviour to keep: a reasoning model called with a small max-tokens budget returns a length finish reason and an empty body, which looks like success, so truncation detection is mandatory.

## Slide 20
VERIFICATION 7 · GUARDS AND INJECTION (S6)
Do the guards fire, and only then?
验证 7：守卫与故障注入
Every injected fault was caught, once, with no false alarms
detection 1.00 (15/15) · false positives 0/3 · thresholds block 0.0777 / warn 0.0867
How we measured
测量方法
calibrated drift thresholds on real corpora (24 on-topic vs 8 real
off-topic papers, 15 building the centroid and 9 held back);
injected six scenarios three times each
Results
实测结果
seed-corpus centroid separates the distributions: on-topic
0.0885–0.2149 vs off-topic 0.0330–0.0670, gap 0.0215 →
TPR 1.0 / FPR 0.0; five families 3/3
Caveat — keyword scope: no threshold worked
Formulas
计算公式
block = (min_on + max_off) / 2
= (0.0885 + 0.0670) / 2 = 0.0777
阈值取间隙中点
warn = min_on × (1 − margin)
= 0.0885 × 0.98 = 0.0867
预警取正样本下界
separable: min_on > max_off
可分性判据
TPR = TP/(TP+FN) · FPR = FP/(FP+TN)
检出率与误报率
Impact
结论影响
scope representation and calibration became frozen rules; retrieval and guard share one scorer
Guards proven
Phase 0 Progress Report · EE5003 · NUS
20 / 21
Notes: Calibration came first, on real corpora: twenty-four on-topic papers against eight real off-topic ones, with an honest hold-out — the first fifteen build the centroid by leave-one-out and the last nine are held back as the inspected artefacts. With the seed-corpus centroid on-topic scores run from 0.0885 to 0.2149 and off-topic from 0.0330 to 0.0670, so the two distributions separate by a gap of 0.0215. The block threshold is the midpoint of that gap, 0.0885 plus 0.0670 over two, which is 0.0777. The warn threshold is the lower bound of the on-topic distribution discounted by a two percent margin, 0.0885 times 0.98, which is 0.0867. That gives a true-positive rate of one and a false-positive rate of zero.
The counter-example is the more useful slide content: with a keyword-string scope the distributions overlapped — 0.000 to 0.165 on-topic against 0.000 to 0.029 off-topic — and no threshold worked; the best zero-false-positive sweep still gave 0.88 true positives against 0.29 false positives. And the first version of the warn rule, block times 1.5, landed at 0.12, inside the on-topic distribution, producing three false alarms out of three normal runs. Hence the rule is frozen: warn is the on-topic lower bound times one minus the margin, never block times a constant. Six scenarios were then injected three times each, entirely offline, and all five fault families were detected three out of three with no false alarms on the normal runs.

## Slide 21
VERIFICATION 8 · METRICS (S7)
Can the numbers be recomputed from events?
验证 8：指标可从事件复算
Every headline number is recomputed from events and reproduces by hand
grounding 0.7949 (31/39) · hallucination 0.2051 (8/39) · cost $0.006294 per run · hand check 16 / 1 / 6 / 23
How we measured
测量方法
aggregated five metrics from the event log only, never from
summary files, over a defined campaign (last 3 runs per
scenario, last 2 report runs, cold start)
Results
实测结果
citation-resolvable rate 1.0; injection TPR 1.0; FPR 0.0;
topicality 0.0699; cold-start cost max $0.012589; the hand
check (16 / 1 / 6 / 23) matched the event statistic
Caveat — labels are model-self-reported (llm_self_label)
Formulas
计算公式
grounding = supported / verifiable = 0.7949
支持率
hallucination = 1 − grounding = 0.2051
幻觉率 = 1 − 支持率
severe = contradicted / verifiable = 0.0513
严重幻觉率
cost_mean = Σ cost / runs = $0.006294
单次平均成本
Impact
结论影响
three instrumentation points were added; a gold fact set + cross-vendor judge is next
Numbers auditable
Phase 0 Progress Report · EE5003 · NUS
21 / 21
Notes: Five metrics are aggregated from the event log only, never from summary files, over a defined campaign: the last three runs per scenario, the last two report runs, and the cold start. Grounding is supported over verifiable, 31 over 39, which is 0.7949; hallucination is its complement, 8 over 39, 0.2051; severe hallucination is contradicted over verifiable, 2 over 39, 0.0513; topicality is the mean cosine between claim and scope, 0.0699; mean cost per run is $0.006294 with a cold-start maximum of $0.012589. The citation-resolvable rate is 1.0, injection detection is 1.0 and the false-positive rate is 0.0, none of which depend on a model. Hand-checking one run against its raw claim file gave 16 supported, 1 contradicted, 6 unsupported and 23 verifiable, matching the event-side statistic exactly, which is what makes the numbers auditable. One caveat to keep in the write-up: Phase 0 support labels are model-self-reported, so grounding is not yet independently verified; the deterministic citation-resolvable rate of 1.0 is the hard lower bound, and a gold fact set with a cross-vendor judge is the next step.